## Slide 1: Computational Photography: Cameras + Optics
Connelly Barnes

## Slide 2: Cameras + Optics
Today:
  Camera obscura / pinhole camera
  Cameras with lenses
  Modeling camera projections

## Slide 3: Art around UVA
Fralin Art Museum
Kluge-Ruhe Aboriginal Art Museum
McGuffey Art Center
Second Street Gallery

## Slide 4: Camera Obscura
Camera is Latin for chamber/room, obscura means dark
[Slide content from Efros]

## Slide 5: Camera Obscura
Used by Euclid (300 B.C.) to show light travels in straight rays
[Image from Efros]

## Slide 6: Pinhole Camera
Illustration by Steve Seitz
- Blurry image results if all rays reach film

## Slide 7: Pinhole Camera
Illustration by Steve Seitz
- Pinhole camera has small aperture size.
- All objects are in focus – depth of field infinite
Center of Projection

## Slide 8: New Worlds Mission (NASA)

## Slide 9: Pinhole Camera
do
ho
hi
di
hi
ho
di
do
=
Similar triangles gives optics law:
Object
Image
Screen

## Slide 10: Pinhole Camera
do
ho
hi
di
Fix object size and imaging plane distance:
hi
1
do
∝

## Slide 11: Perspective

## Slide 12: Human Visual System
Müller-Lyer Illusion
The human brain attempts to invert the 3D => 2D projective mapping.

## Slide 13: Limitations of Pinhole Camera
Pros:
  Hard to detect (surveillance)
  Infinite depth of field
Cons:
  Not much light => higher noise
  Diffraction for small aperture size

## Slide 14: Limitations of Pinhole Camera

## Slide 15: Lenses
Let in more light!
do
f
di
Object
Image
Focal Length
Focal Point

## Slide 16: Lenses
Thin lens equation:
do
f
di
1
f
1
do
=
1
di
+

## Slide 17: Focal Length
do
f
di
- Reported in mm, e.g. 50 mm lens.
- For zoom lenses, a range, e.g. 18-55 mm.

## Slide 18: Angle of View (Field of View)
Focal Point
Sensor Dimension d
Focal length f
α
α = 2 tan-1 [d/(2f)] ≈ d / f (radians)

## Slide 19: Angle of View (Field of View)
[Slide content from Fredo Durand]

## Slide 20: Shutter Speed
Expressed in fractions of a second, e.g. 1/100 sec
If shutter is open longer, integrates across time
If shutter open too short, can cause noise

## Slide 21: High Shutter Speed
[Photo by Terence Tam]

## Slide 22: High Shutter Speed
[Photo by Terence Tam]

## Slide 23: High Shutter Speed
[Photo by Jasper Nance]

## Slide 24: Very High Shutter Speed
Trillion FPS Camera

## Slide 25: Low Shutter Speed
[Photo by Zach Heller]

## Slide 26: Low Shutter Speed
[Photo by Evan ‘thevlue’]

## Slide 27: Low Shutter Speed
Star Trails

## Slide 28: Aperture
[Slide content from Fredo Durand]
- Trades off more/less light.
- Controls depth of field

## Slide 29: Depth of Field
[mmphotography.it]

## Slide 30: Depth of Field
[mmphotography.it]

## Slide 31: Depth of Field
[Photo by Neil Halin]

## Slide 32: Aperture
- Only one depth where objects are exactly in focus
- Other depths project to a circle on the film
Aperture controls depth of field
Illustration by Steve Seitz

## Slide 33: How to Adjust Focus?
Aperture controls depth of field
Denoted in f number (“f-stop”)

## Slide 34: ISO
Analog gain factor
Normally 200-1600
Each time you double ISO the camera only needs half as much light
But, photon and sensor noise increases

## Slide 35: ISO
[Photo by FedEx]

## Slide 36: ISO
[Photo by FedEx]

## Slide 37: How to Control Exposure
    Trade off aperture, shutter speed, ISO to get desired exposure
    Want signal to not overflow (overexposed)
    Typically do not want noise
      Use tripod!

## Slide 38: How to Control Exposure
Aperture size decreased => less light let in.
What if we want more light?
Can keep shutter open longer.
For pro cameras:
  Aperture priority – you set aperture, camera sets shutter speed
  Shutter priority – you set shutter speed, camera sets aperture.

## Slide 39: How to Adjust Focus?
Lytro

## Slide 44: Homogeneous Coordinates
Used in graphics/vision when transforming geometry prior to projection on the screen.
  e.g. to translate (T), scale (S), rotate (R), then perspective project (P) a point p:
  q = PRSTp
PRST 4x4 matrices, pq 4x1 vectors

## Slide 45: Homogeneous Coordinates
Transformation matrices found in OpenGL documentation:
  glTranslate
  glScale
  glRotate
  Derivation of Rotation Matrices in R3
Can look at some of these on the board

## Slide 46: Conclusion
Discussed:
  Camera obscura / pinhole camera
  Cameras with lenses
  Modeling camera projections
I should:
  Get us DSLR and Lytro cameras to play with
  Post the first assignment