## Slide 1: CS 6501: 3D Reconstruction and Understanding Camera Models and Calibration
Connelly Barnes
Slides from Fei Fei Li, Juan Carlos Niebles, Jason Lawrence, Szymon Rusinkiewicz, David Dobkin, Adam Finkelstein, Tom Funkhouser

## Slide 2: Outline
Human eyes
  How do they sense light?
  Visible light and human color perception
Electronic eyes
  How do they sense light?
  Image and color representation
Camera models
  Pinhole camera and lenses
  Transformation matrices
  Camera calibration

## Slide 3: Image Formation
Digital Camera
The Eye
Film
Slide by Efros

## Slide 4: The Eye
The human eye is a camera!
  Iris - colored annulus (ring) with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Slide by Steve Seitz

## Slide 5: Ordinary Human Vision (Trichromatism)

## Slide 6: Perceptual Sensitivity

## Slide 7: Outline
Human eyes
  How do they sense light?
  Visible light and human color perception
Electronic eyes
  How do they sense light?
  Image and color representation
Camera models
  Pinhole camera and lenses
  Transformation matrices
  Camera calibration

## Slide 8: Electronic Eyes: Sensor Arrays
CMOS sensor
Slide by Efros
CCD sensor

## Slide 9: Sampling and Quantization

## Slide 10: Outline
Human eyes
  How do they sense light?
  Visible light and human color perception
Electronic eyes
  How do they sense light?
  Image and color representation
Camera models
  Pinhole camera and lenses
  Transformation matrices
  Camera calibration

## Slide 11: Color Image
R
G
B
Color
channels

## Slide 12: Images in Python
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column
Image as array: h x w x channels
  I[y,x,channel]
Red channel, upper left corner:
  MATLAB: I(1,1,1), Python: I[0,0,0]
Common ranges of pixel values:
Float (typical range: [0, 1])
Unsigned 8-bit integer (range: [0, 255])
Which is easier to work with?

## Slide 13: Color spaces: RGB
0,1,0
0,0,1
1,0,0
Image from: http://en.wikipedia.org/wiki/File:RGB_color_solid_cube.png
Some drawbacks
Strongly correlated channels
Non-perceptual
Default color space
R
(G=0,B=0)
G
(R=0,B=0)
B
(R=0,G=0)

## Slide 14: Color spaces: HSV
Intuitive color space
H
(S=1,V=1)
S
(H=1,V=1)
V
(H=1,S=0)

## Slide 15: Color spaces: L*a*b*
“Perceptually uniform” color space
L
(a=0,b=0)
a
(L=65,b=0)
b
(L=65,a=0)
Python tip: skimage.color can convert between color spaces

## Slide 16: Color spaces: Grayscale
From the video coding standards PAL and NTSC, convert RGB to Y:
  Y [Luminance] = 0.30 R + 0.59 G + 0.11 B

## Slide 17: Outline
Human eyes
  How do they sense light?
  Visible light and human color perception
Electronic eyes
  How do they sense light?
  Image and color representation
Camera models
  Pinhole camera and lenses
  Transformation matrices
  Camera calibration

## Slide 18: Pinhole Camera
Illustration by Steve Seitz
- Pinhole camera has small aperture size.
- All objects are in focus – depth of field infinite
Center of Projection

## Slide 19: Pinhole Camera
do
ho
hi
di
hi
ho
di
do
=
Similar triangles gives optics law:
Object
Image
Screen

## Slide 20
do
ho
hi
di
Fix object size and imaging plane distance:
hi
1
do
∝
Pinhole Camera

## Slide 21: Perspective

## Slide 22: Limitations of a Physical Pinhole Camera
Pros:
  Infinite depth of field
  Reasonable math model for 2D/3D correspondence (but, typically need to compensate for lens distortion)
Cons:
  Not much light => higher noise
  Diffraction for small aperture size

## Slide 23: Lenses
Let in more light!
do
f
di
Object
Image
Focal Length
Focal Point

## Slide 24: Lenses
Thin lens equation:
1
f
1
do
=
1
di
do
f
di
Object
Image
Focal Length
Focal Point
+

## Slide 25: Lenses
do
f
di
Object
Image
Focal Length
Focal Point
- Focal length reported in mm, e.g. 50 mm lens.
- For zoom lenses, a range, e.g. 18-55 mm.

## Slide 26: Angle of View (Field of View)
Focal Point
Sensor Dimension d
Focal length f
α
α = 2 tan-1 [d/(2f)] ≈ d / f (radians)

## Slide 27: Angle of View (Field of View)
[Slide content from Fredo Durand]

## Slide 28: Shutter Speed
Expressed in fractions of a second, e.g. 1/100 sec
If shutter is open longer, integrates across a longer time
If shutter open too short, can cause noise

## Slide 29: Shutter Speed
[Photo by Terence Tam]
Was the shutter open a long time or a short time?

## Slide 30: Shutter Speed
[Photo by Zach Heller]
Was the shutter open a long time or a short time?

## Slide 31
[Slide content from Fredo Durand]
- Trades off more/less light.
- Controls depth of field
Aperture
f/1.4
f/16

## Slide 32: Outline
Human eyes
  How do they sense light?
  Visible light and human color perception
Electronic eyes
  How do they sense light?
  Image and color representation
Camera models
  Pinhole camera and lenses
  Transformation matrices
  Camera calibration

## Slide 33: 2D Transformations: Translation

## Slide 34: 2D Transformations: Translation

## Slide 35: 2D Transformations: Scaling

## Slide 36: 2D Transformations: Rotation
Inverse of any rotation matrix R is just RT.

## Slide 37: Transformation Matrices
Slide from Fei-Fei Li and Juan Carlos Niebles

## Slide 38: Homogeneous Coordinates
Slide from Fei-Fei Li and Juan Carlos Niebles

## Slide 39: Homogeneous Coordinates
Slide from Fei-Fei Li and Juan Carlos Niebles

## Slide 40: 2D Translation Using Homogeneous Coordinates

## Slide 41: 2D Transformations: Scaling

## Slide 42: 2D Rotation Using Homogeneous Coordinates

## Slide 43: 3D Homogeneous Coordinates
Represent a 3D point as:
If last coordinate ends up non-one, convention is to divide by it:

## Slide 44: 3D Homogeneous Coordinates
Translation by (tx, ty, tz):

## Slide 45: 3D Homogeneous Coordinates
Scaling by (sx, sy, sz):

## Slide 46: 3D Homogeneous Coordinates
Rotation around z axis:

## Slide 47: Outline
Human eyes
  How do they sense light?
  Visible light and human color perception
Electronic eyes
  How do they sense light?
  Image and color representation
Camera models
  Pinhole camera and lenses
  Transformation matrices
  Camera calibration

## Slide 48: Camera Calibration
Determine mathematical relationship between points in 3D and their projection onto a 2D imaging plane
[Tsukuba]
3D scene
2D image
Imaging
device

## Slide 49: Stereo Vision

## Slide 50: Principal Application: 3D Scene Reconstruction
[Zhu and Humphreys]

## Slide 51: Camera Calibration
Take pictures of scene with known 3D structure and solve for free parameters in projection:
x
y
z

## Slide 52: Camera Calibration
Need to address these issues:
  How do we model the way a camera projects 3D points onto a 2D image?
  How many parameters are involved in this projection and what is their relationship (linear/non-linear)?
  Which measurements/how many allow us to robustly estimate these parameters?

## Slide 53: Pinhole Camera Model: Camera Matrix
Camera matrix: a 3x4 matrix that transforms from 3D scene points (x, y, z) to 2D screen points (x/w, y/w):
How many free parameters in the camera matrix?

## Slide 54: Pinhole Camera Model
Can rewrite the camera matrix in terms of intrinsic and extrinsic parameters.
How many intrinsic parameters?
How many extrinsic parameters?
How many parameters in total?
K=
Intrinsic matrix
, focal length in pixels, skew between x and y axes (often zero), , principal point (typically center of image).
World coordinates
Screen coordinates

## Slide 55: Real Camera Model: Radial Distortion
Photo by Renaud Leon, Creative Commons Licensed

## Slide 56: Real Camera Model: Radial Distortion
These nonlinear effects cannot be represented by a matrix
Additional intrinsic parameters (for more accuracy, can also include r4, r6 terms)

## Slide 57: Camera Calibration
Take pictures of scene with known 3D structure and solve for free parameters in projection:
x
y
z

## Slide 58: Calibration Algorithms
Particular method used depends on:
  What data is available!
  Intrinsics only vs. extrinsics only vs. both
  Camera model being used (pinhole, affine, etc.)
  Typical model (e.g. OpenCV): pinhole + radial distortion

## Slide 59: Camera Calibration: Example #1
Given:
  3D <=> 2D correspondences
  Pinhole camera model (no radial distortion)
Convert camera matrix into system of equations:

## Slide 60: Camera Calibration: Example #1
Convert camera matrix into system of equations:
.
.
.
Known screen point 1
Known 3D point 1
Can solve with nonlinear least squares (e.g. scipy.optimize.least_squares)

## Slide 61: Camera Calibration in Practice
Camera Calibration with OpenCV
YouTube Video