## Slide 1: CS 4501: Introduction to Computer Vision Camera Calibration and Stereo Cameras
Connelly Barnes
Slides from Fei Fei Li, Juan Carlos Niebles, Jason Lawrence, Szymon Rusinkiewicz, David Dobkin, Adam Finkelstein, Tom Funkhouser

## Slide 2: Outline
Camera calibration
Overview of 3D vision
Camera demos
Stereo cameras
  Epipolar geometry
  Parallel stereo cameras and rectification
Structure from motion: Photo Tourism

## Slide 3: Camera Calibration
Determine mathematical relationship between points in 3D and their projection onto a 2D imaging plane
[Tsukuba]
3D scene
2D image
imaging
device

## Slide 4: Stereo Vision

## Slide 5: Principal Application: 3D Scene Reconstruction
[Zhu and Humphreys]

## Slide 6: Camera Calibration
Take pictures of scene with known 3D structure and solve for free parameters in projection:
x
y
z

## Slide 7: Camera Calibration
Need to address these issues:
  How do we model the way a camera projects 3D points onto a 2D image?
  How many parameters are involved in this projection and what is their relationship (linear/non-linear)?
  Which measurements/how many allow us to robustly estimate these parameters?

## Slide 8: Pinhole Camera Model: Camera Matrix
Camera matrix: a 3x4 matrix that transforms from 3D scene points (x, y, z) to 2D screen points (x/w, y/w):
How many free parameters in the camera matrix?

## Slide 9: Pinhole Camera Model
Can rewrite the camera matrix in terms of intrinsic and extrinsic parameters.
How many intrinsic parameters?
How many extrinsic parameters?
How many parameters in total?
K=
Intrinsic matrix

## Slide 10: Real Camera Model: Radial Distortion
Photo by Renaud Leon, Creative Commons Licensed

## Slide 11: Real Camera Model: Radial Distortion
These nonlinear effects cannot be represented by a matrix
Additional intrinsic parameters (for more accuracy, can also include r4, r6 terms)

## Slide 12: Camera Calibration
Take pictures of scene with known 3D structure and solve for free parameters in projection:
x
y
z

## Slide 13: Calibration Algorithms
Particular method used depends on:
  What data is available!
  Intrinsics only vs. extrinsics only vs. both
  Camera model being used (pinhole, weak-perspective, affine, etc.)

## Slide 14: Camera Calibration: Example #1
Given:
  3D <=> 2D correspondences
  General pinhole camera model (11-parameter, no radial distortion)
Convert camera matrix into system of equations:

## Slide 15: Camera Calibration: Example #1
Convert camera matrix into system of equations:
.
.
.
Known screen point 1
Known 3D point 1

## Slide 16: Camera Calibration: Example #1
Multiply by denominator to get linear system:
c11
c12
c13
c34
⋮

## Slide 17: Camera Calibration: Example #1
Standard linear least squares methods for Ax=0 will give the solution x=0
Instead, look for solution with ||x||=1 (recall our solution is valid up to global scale)
That is, minimize ||Ax||2 subject to ||x||2 =1

## Slide 18: Camera Calibration: Example #1
Eigenvector ei, eigenvalue
+ +…

## Slide 19: Camera Calibration: Example #1
to minimize subject to set and all others to
Summary: least squares solution is eigenvector of corresponding to minimum eigenvalue

## Slide 20: Camera Calibration: Example #1.5
Incorporating additional constraints into camera model
  No shear, no scale (rigid-body motion)
  Square pixels
These lead to nonlinear constraints on camera parameters

## Slide 21: Camera Calibration: Example #1.5
Option 1: solve for general perspective model as before, then find closest solution that satisfies constraints
Option 2: nonlinear least squares
  Usually “gradient descent” techniques
  Common implementations available (e.g., MATLAB’s optimization toolbox, scipy.optimize.minimize)

## Slide 22: Camera Calibration: Example #2
Incorporating radial distortion
Option 1:
  Find distortion first (use straight lines in calibration target)
  Warp image to eliminate distortion
  Run (simpler) perspective calibration
Option 2: nonlinear least squares

## Slide 23: Camera Calibration in Practice
Camera Calibration with OpenCV
YouTube Video

## Slide 24: camera calibration: example #4
what if 3D points are not known?
Structure from Motion!
unknowns: 3N + 6C (extrinsics only)
knowns: 2NC
overconstrained when: 2NC > 3N + 6C

## Slide 25: multi-camera geometry
epipolar geometry - relationship between observed positions of points in multiple cameras
assumptions:
  2 cameras
  known intrinsics and extrinsics (i.e., fully calibrated rig)

## Slide 26: Outline
Camera calibration
Overview of 3D vision (separate slide deck)
Camera demos
Stereo cameras
  Epipolar geometry
  Parallel stereo cameras and rectification
Structure from motion: Photo Tourism

## Slide 27: Camera Demos
Demo of stereo camera (StereoLabs ZED camera)
Demo of structured light depth sensor (Kinect)
  What it looks like in the infrared spectrum
Demonstrate depth discontinuities / occlusions

## Slide 28: Outline
Camera calibration
Overview of 3D vision (separate slide deck)
Camera demos
Stereo cameras
  Epipolar geometry
  Parallel stereo cameras and rectification
Structure from motion: Photo Tourism

## Slide 29: Stereo Matching

## Slide 30
Slide from Jason Lawrence

## Slide 31
Slide from Jason Lawrence

## Slide 32
Slide from Jason Lawrence

## Slide 33
Slide from Jason Lawrence

## Slide 34
Slide from Jason Lawrence

## Slide 35
Slide from Jason Lawrence

## Slide 36
Slide from Jason Lawrence

## Slide 37
Slide from Jason Lawrence

## Slide 38
Slide from Jason Lawrence

## Slide 39
Slide from Jason Lawrence
Assumes normalized image coordinates:
  Measure coordinates in scene/world coordinate units (e.g. mm)
  Relative to the pinhole camera center.

## Slide 40
Slide from Jason Lawrence

## Slide 41: Outline
Camera calibration
Overview of 3D vision (separate slide deck)
Camera demos
Stereo cameras
  Epipolar geometry
  Parallel stereo cameras and rectification
Structure from motion: Photo Tourism

## Slide 42: Parallel Stereo Cameras

## Slide 43: Parallel Stereo Cameras

## Slide 44: Parallel Stereo Cameras: Disparity
Disparity: displacement in pixels of the apparent motion of a 3D scene point as we switch between the left and right view of a stereo camera.
Examples from Middlebury stereo dataset
Discussion: how might this disparity information be useful?

## Slide 45: Parallel Stereo Cameras: Depth from Disparity

## Slide 46: Stereo Correspondence Problem
Usually assume rectified (parallel, upright) cameras.
For each pixel in the left camera image, find its disparity (x pixels displacement of the corresponding point in the right image).
  Dense matching
Edges, corners: easier.
Challenge: flat regions.
  How might we determine where a flat region went from a left image to a right image?

## Slide 47: Stereo Correspondence Problem
Typical algorithmic approach described in Szeliski 11.3:
  Compute matching cost
  Aggregate matching costs
  Compute/optimize disparities
  (Optional) refine disparities

## Slide 48: Stereo Correspondence Problem
From Scharstein and Szeliski 2002

## Slide 49: Stereo Correspondence: Matching Cost
Disparity Space Image (DSI): A 3D array that measures at (x, y, d) the cost of assigning disparity d to pixel (x, y).
Typically a simple measure of dissimilarity such as sum of squared difference (SSD), or sum of absolute difference (SAD).

## Slide 50: Stereo Correspondence: Matching Cost
Disparity Space Image (DSI): A 3D array that measures at (x, y, d) the cost of assigning disparity d to pixel (x, y).
(x, y) slice through the DSI for d = 10
From Scharstein and Szeliski 2002

## Slide 51: Stereo Correspondence: Matching Cost
Disparity Space Image (DSI): A 3D array that measures at (x, y, d) the cost of assigning disparity d to pixel (x, y).
From Scharstein and Szeliski 2002
(x, y) slice through the DSI for d = 16

## Slide 52: Stereo Correspondence: Matching Cost
Disparity Space Image (DSI): A 3D array that measures at (x, y, d) the cost of assigning disparity d to pixel (x, y).
From Scharstein and Szeliski 2002
(x, y) slice through the DSI for d = 21

## Slide 53: Stereo Correspondence: Matching Cost
Disparity Space Image (DSI): A 3D array that measures at (x, y, d) the cost of assigning disparity d to pixel (x, y).
(x, d) slice through the DSI
From Scharstein and Szeliski 2002

## Slide 54: Stereo Correspondence Problem
From Scharstein and Szeliski 2002

## Slide 55: Stereo Correspondence: Aggregation
Disparity Space Image (DSI): A 3D array that measures at (x, y, d) the cost of assigning disparity d to pixel (x, y).
Convolve DSI with 2D or 3D filter to aggregate information.
Simple example: convolve with 2D Gaussian with given σ
  Larger window size: better handling of flat regions
  Smaller window size: better detail, depth discontinuities
Compute disparities:
  Choose at each pixel disparity d with min cost after aggregation
More advanced methods reviewed in Szeliski 11.3, 11.4

## Slide 56: Stereo Correspondence: Window Size (or σ)
From Scharstein and Szeliski, 1996
3 pixel window
20 pixel window
Nonlinear Diffusion

## Slide 57: Stereo Rectification

## Slide 58: Stereo Rectification

## Slide 59: Stereo Rectification

## Slide 60: Applications
Depth from Stereo (YouTube)
3D Reconstruction from Stereo (YouTube)

## Slide 61: Implementation in OpenCV
OpenCV includes:
  Camera calibration
  Epipolar geometry
  Stereo rectification
  Finding stereo correspondences using block matching
  …

## Slide 62: Outline
Camera calibration
Overview of 3D vision (separate slide deck)
Camera demos
Stereo cameras
  Epipolar geometry
  Parallel stereo cameras and rectification
Structure from motion: Photo Tourism