## Slide 1: Overview of 3D Computer Vision
Slides by Connelly Barnes, Jason Lawrence, Szymon Rusinkiewicz
CS 4501

## Slide 2: 3D perception: stereo

## Slide 3: 3D perception: stereo
experiments show that absolute depth estimation not very accurate
  low “relief” judged to be deeper than it is
relative depth estimation very accurate
  can judge which object is closer for stereo disparities of a few seconds of arc

## Slide 4: 3D computer vision
recover representation of 3D shapes from (primarily) images:
[Debevec et al.]

## Slide 5: 3D data types
point data
volumetric data
surface data

## Slide 6: 3D data types: point data
“point clouds”
advantage: simplest data type
disadvantage: no information on adjacency/connectivity

## Slide 7: 3D data types: volumetric data
regularly-spaced grid in (x,y,z): “voxels”
for each grid cell, store
  occupancy (binary: occupied/empty)
  density
  other properties
popular in medical imaging
  CAT scans
  MRI

## Slide 8: 3D data types: volumetric data
advantages:
  can “see inside” objects
  uniform sampling: simpler algorithms
disadvantages:
  lots of data
  wasteful if only storing surface
  most “vision” sensors / algorithms return point or surface data

## Slide 9: 3D data types: surface data
polyhedral
  piecewise planar
  polygons connected together
  most popular: “triangle meshes”
smooth
  higher-order (quadratic, cubic, etc.) curves
  Bezier patches, splines, NURBS, subdivision surfaces, etc.

## Slide 10: 3D data types: surface data
advantages:
  preserves adjacency information
  usually returned by vision sensors / algorithms
disadvantages:
  difficult to define for translucent objects
  non-uniform parameterization
  non-topology-preserving algorithms difficult

## Slide 11: 2.5-D data
color along each ray
depth along each ray
http://www.ixbt.com

## Slide 12: 2.5-D data
image: stores an intensity / color along each set of regularly-spaced rays in space
range images: stores a depth along each of a set of regularly-spaced rays in space
not a complete 3D description: does not store objects occluded (from some view)
view-dependent scene description

## Slide 13: 2.5-D data
this is what most sensors / algorithms actually return
advantages:
  uniform parameterization
  adjacency / connectivity information
disadvantages:
  does not represent entire object
  view dependent

## Slide 14: 2.5-D data
range images
range surfaces
depth images
depth maps
height fields
2.5-D images
surface profiles
xyz maps
...

## Slide 15: range acquisition taxonomy
Range acquisition
Contact
Transmissive
Reflective
Non-optical
Optical
Industrial CT
Mechanical (CMM, jointed arm)
Radar
Sonar
Ultrasound
MRI
Ultrasonic trackers
Magnetic trackers
Inertial (gyroscope, accelerometer)

## Slide 16: touch probes
jointed arms with angular encoders
return position, orientation of tip
Faro Arm - Faro Technologies, Inc.

## Slide 17: range acquisition taxonomy
Optical methods
Passive
Active
Shape from X:
stereo
motion
shading
texture
focus
defocus
Active variants of passive methods
Stereo w. projected texture
Active depth from defocus
Photometric stereo
Time of flight
Triangulation

## Slide 18: optical range acquisition methods
advantages:
  non-contact
  safe
  usually inexpensive
  usually fast
disadvantages:
  sensitive to transparency
  confused by specularity and interreflection
  texture (helps some methods, hurts others)

## Slide 19: stereo
find feature in one image, search for corresponding feature in other image:

## Slide 20: stereo
advantages:
  passive
  cheap hardware (2 cameras)
  intuitive analogue to human vision
disadvantages:
  only acquire good data at “features”
  sparse, relatively noisy data (correspondence is hard)
  bad around silhouettes
  confused by non-diffuse surfaces
variant: incorporate multiple cameras into multibaseline stereo to reduce ambiguity

## Slide 21: shape (structure) from motion
“limiting case” of multibaseline stereo
track a feature in a sequence of images
for N frames and F features have 2NF knowns and 6N+3F unknowns
[Tomasi and Kanade]

## Slide 22: shape (structure) from motion
advantages:
  feature tracking easier than correspondence in far-away views
  mathematically more stable (large baseline)
disadvantages:
  does not accommodate object motion
  still problems in areas of low texture, non-diffuse regions, and around silhouettes

## Slide 23: shape from shading
problem: ambiguity
[Pentland]

## Slide 24: shape from shading
advantages:
  single image
  no correspondences
  analogue in human vision
disadvantages:
  mathematically unstable
  can’t have texture
“photometric stereo” (active method) more practical than passive version

## Slide 25: shape from texture
mathematically similar to shape from shading, but uses distortion of texture

## Slide 26: shape from texture
analogue to human vision
same disadvantage as shape from shading

## Slide 27: shape from focus
shape from focus: at which focus setting is a given image region sharpest?
shape from defocus: how out-of-focus is each image region?
passive versions rarely used
active depth from defocus can be made practical

## Slide 28: active optical methods
advantages:
  can usually obtain dense data
  usually much more robust and accurate than passive techniques
disadvantages:
  introduces light into the scene
  not motivated by human vision
[Digital Michaelangelo Project]

## Slide 30: terminology
range acquisition, shape acquisition, rangefinding, range scanning, 3D scanning
alignment, registration
surface reconstruction, 3D scan merging, scan integration, surface extraction
3D model acquisition