## Slide 1: CS 4501: Introduction to Computer Vision Augmented and Virtual Reality
Connelly Barnes
Some slides from Fei-Fei Li / Andrej Karpathy / Justin Johnson

## Slide 2: Outline
Augmented reality
Virtual reality

## Slide 3: Augmented and Virtual Reality
Augmented reality: Live view of a physical, real-world environment augmented with virtual objects.
Virtual reality: a headset is used to generate synthetic images (sounds) that replace the real environment.
Image from Wangxiang Tuxing
Image from Wikipedia / HTC

## Slide 4: Augmented Reality Videos
Microsoft Hololens
  5 color cameras, 1 depth camera
  1 Inertial Measurement Unit
    Measures linear/angular motion: gyroscopes and accelerometers
"The Future of Augmented Reality"

## Slide 5: SLAM (Simultaneous Localization And Mapping)
SLAM: Constructing or updating a map of an unknown environment while also tracking an agent’s location in the environment.

## Slide 6: LSD-SLAM
https://www.youtube.com/watch?v=GnuQzP3gty4

## Slide 7: LSD-SLAM Overview

## Slide 8: How to Represent Rotations?
SO(3): group of all rotations about the origin in 3D Euclidean space
  “Special orthogonal group”
  3x3 orthogonal matrices (AT = A-1) with determinant 1
  Could represent rotation directly as a 3x3 matrix R, but
    This requires 9 entries to represent rotations (only 3 DOF)
    Accumulated errors can cause matrices to drift from orthogonal

## Slide 9: How to Represent Rotations?
Common solutions:
  Re-orthogonalize matrices (e.g. via SVD)
  Unit quaternions
  Lie algebra so(3): set of 3x3 skew-symmetric matrices.
    Used by LSD-SLAM paper
    “Differential rotations”
    Can map so(3) to SO(3) via matrix exponential
    Matrix exponential:

## Slide 10: How to Represent Rigid Motions?
SE(3): group of 3D rigid motions: translation plus rotation
  “Special Euclidean group”
  Related (via matrix exponential) to
  se(3): the Lie algebra of differential translations and rotations.
For more details, see tutorial on Lie groups for 2D/3D transforms

## Slide 11: Software: ARToolKit
Tracking
  Barcodes
  FREAK --- Fast REtinA Keypoints, a SIFT-inspired feature
Camera calibration
Stereo cameras
See-through displays
Widely used open source tracking library first released in 1999

## Slide 12: Augmented Reality Application (ARToolKit)
Simple example:
  Use square template markers
  ARSimple / simpleLite video
  ARSimple code
Intrinsic camera matrix:
  ARToolKit knows for popular iOS cameras
  Otherwise, may need to do camera calibration for best results

## Slide 13: Software: ARToolKit
Demo

## Slide 14: Augmented Reality + Faces
Face landmark detection example
Snapchat lenses

## Slide 15: Outline
Augmented reality
Virtual reality

## Slide 16: History
The Sword of Damocles: VR/AR head mounted display
  Ivan Sutherland and Bob Sproull, 1965 to 1968
“The ultimate display would, of course, be a room within which the computer can control the existence of matter. A chair displayed in such a room would be good enough to sit in. Handcuffs displayed in such a room would be confining, and a bullet displayed in such a room would be fatal.” – Ivan Sutherland

## Slide 17: Google Cardboard
Android Phone + $15 kit

## Slide 18: Example: Oculus Rift
Example Interactions
Sensors:
  Gyroscope / accelerometer / magnetometer
  Infrared LEDs
  Tracking cameras

## Slide 19: VR Applications
Tilt Brush

## Slide 20: Rendering
Game engines (e.g. Unity)
OpenGL / WebGL / Direct3D

## Slide 21: University of Virginia Resources
Clemons Library / Robertson Media Center
  HTC Vive
  Oculus Rift